## Slide 1
＊
＊
＊
＊
＊
Objective
Equipment and Materials
NIHL is a common occupational disorder caused by prolonged exposure to high-intensity noise. In military personnel, exposure to blast noise during training and operations can result in irreversible cochlear hair cell damages and permanent hearing impairment. Because effective treatment is limited, prevention is essential. This study evaluated noise exposure during 84mm recoilless rifle firing.
Cochlear Hair Cell
Normal
Abnormal
Figure1. Changes in Cochlear Hair Cells
Caused by Noise Exposure
http://www.doyukai.com/medical/128.html
Noise Exposure Assessment and Evaluation of Hearing Protection Effectiveness during
84mm Recoilless Rifle Firing
N. Ogata, S. Yamada, K. Ito, K. Kaminishi, W. Nagata, T. Nara, T. Nihongi, S. Kurihara,
M. Kawasaki
Military Medicine Research Unit, Test & Evaluation Command, Japan Ground Self-Defense Force
Shooter
Assistant
Gunner
0 m
reference point
Figure 2. Measurement Setup
5 m
Head-model sensor
Earplug
Earmuff
Hearing Protection Devices
Pencil-type sound sensor
(used as a monitor）
Statistic Analysis
Two-group comparison: Mann-Whitney U test
Three-group comparison: Tukey’s multiple comparison test
Moise Exposure Evaluation Criteria
152 dB ( Japanese Occupational Health Society guideline)
Table 1. Comparison of Weapons |  | 
Item | 84RR(B) | 84RR(C)
Image |  | 
Weight | 10.4 kg | 7.0 kg
Continuous firing capacity |  | Automatic trajectory calculation / Automatic aiming adjustment
Noise-induced hearing loss (NIHL) is a major health concern among military personnel. To assess the current situation, we measured and analyzed acoustic noise generated during the use of military equipment.
Background
Weapon Systems: 84mm Recoilless Rifle (84RR), Models B and C
Ammunition: Training Projective (TP), High-Explosive (HE) Round,
Hearing Protection Devices: Earplugs(SUREFIRE®), Earmuffs(OPS-CORE®)
Measurement Instruments: Head Simulator sensor system, Pencil-type sound sensor(GRAS®)
Results and Discussions
dB
Double protection provided significantly greater attenuation than earplugs alone.
Peak noise levels were similar between the B and C models.
Increasing distance reduced exposure.
dB
1. Evaluation of Noise Attenuation: Comparison of Hearing Protection Devices
a b c d e
0 m 5 m 0 m 5 m
2. Noise Attenuation with Distance: Comparison Between Weapon Systems
Conclusions
Hearing protection and increased distance effectively reduced sound pressure exposure.
Noise levels may differ by ammunition type, highlighting the need for measurements across multiple ammunition types.
Further studies are needed to optimize hearing protection, establish limits on the number of shots fired, and define safe exposure durations and cumulative exposure.
ａ： Pencil type sensor ： Raw noise
ｂ～ｄ：single protection
ｂ：Earplug ( Right )
ｃ：Earplug ( Left )
ｄ：Earplugs
ｅ：Double protections
＊ Earplugs and Earmuffs
Mounted on the head model sensor under conditions b to e.
firearm：84RR ( B )
Ammunition：TP
Measurement point：10 m
Double protections on the head model sensor.
firearm：84RR ( B )
84RR ( C )
Ammunition：HE
Measurement point：0 m、5 m