## Slide 1
Introduction
Photonics Integrated chip technology for autonomous steering of vital signs sensing
Method
Results
Conclusion
ChenChia Wang1, Feng Jin1, Sudhir Trivedi1, Mark Goncharovsky1, Deepak Patel1, Hayden Diener1, Gary P. Zientara2, Jacob B. Khurgin3, Xue Bai4, Benjamin Punshon-Smith4, and Fow-Sen Choa4
1Brimrose Corp., Baltimore, MD 21152 2US Army Research Institute of Environmental Medicine, Natick, MA 01760
3Dept. of Electrical and Computer Engineering, The Johns Hopkins University, Baltimore, MD 21218 4University of Maryland, Baltimore County, Baltimore, MD 21250
DHA SBIR Phase II Program #HT942524C0069
Autonomous operation, no manual intervention
Visible/ToF cameras locate injured Warfighter
Human Pose Sensing, Body Mesh, Pulse Points coordinates finding and Ranking
Autonomous laser beam steering to selected pulse point: NO moving parts
Optical Speckle-tolerant Laser retrieval of AWF
Onboard GPU AWF analysis and vital signs estimation and display
Photonic IC for device compactness
This project is supported by DHA SBIR Phase II Program under the guidance of Dr. Gary P. Zientara of US Army Research Institute of Environmental Medicine
AWF Detection, Processing, analysis, and Vital Signs Estimations
3D Rendering of Prototype
Pulse Points Coordinates Finding
Images taken from cameras
MMPose, SMPL, PyMAF, applied for pose sensing and pulse point locating.
nVidia Jetson platform as computational core
Operational Applicability : Chest-mount for Role 1 care, Ceiling-/Pole-mount for Role 2 & 3 care
Autonomous operations minimizes human intervention
Continuous bedside autonomous monitoring, no patient restraining
Operational efficiencies, no wires, no cables
Pumping of the heart produces Arterial Waveforms (AWF) along the vasculature.
Prominent Skin surface vibrations caused by AWF, at Pulse Points
Laser sensing of AWF
Analysis of AWF provides vital signs estimations: heartbeat rate (HR), systolic/diastolic blood pressure (SBP/DBP), respiration rate (RR), and core body temperature (TC)
Chest-mount on Combat Medic for Role 1 care
Graphic User Interface
Role 2 and Role 3 Applications
AWF
PIC Design, Fabrication, and Characterization
Laser beam steering, electronic-controlled