## Slide 1
Introduction
Non-contact near-infrared imaging to reveal internal trauma
Method
Results
Conclusion
ChenChia Wang1, Feng Jin1, Sudhir Trivedi1, Mark Goncharovsky1, Deepak Patel1, Hayden Diener1, Gary P. Zientara2, Jacob B. Khurgin3, Xue Bai4, Benjamin Punshon-Smith4, and Fow-Sen Choa4
1Brimrose Corp., Baltimore, MD 21152 2US Army Research Institute of Environmental Medicine, Natick, MA 01760
3Dept. of Electrical and Computer Engineering, The Johns Hopkins University, Baltimore, MD 21218 4University of Maryland, Baltimore County, Baltimore, MD 21250
DHA SBIR Phase II Program #HT9425-24-C-0071
Manual placement over ROI, Autonomous Laser Line Scan over field of view
Electronic controlled laser beam projection over ROI via Photonic IC (PIC), NO moving parts
Time-of-Flight (ToF) camera for standoff distance measurement, aiding hematoma image registration and map forming
Optical Speckle-tolerant Laser sensing of PA signals
Onboard GPU for image processing, forming, and reconstruction and characterization of hematoma map
Photonic IC for device compactness
This project is supported by DHA SBIR Phase II Program under the guidance of Dr. Gary P. Zientara of US Army Research Institute of Environmental Medicine
Human hemoglobin signatures at 790/915 nm
Light beam switching/routing by PIC
3D Rendering of Prototype
Development, validation of hardware components,
Photonics IC design, simulation, validation, and characterizations
Operational Efficiency : non-contact handheld for Role 1 care
Autonomous laser interrogation with minimal manual intervention
Aids rapid POC assessments on invisible hematoma/internal injuries
Wireless communications enable Role 2/3 studies
Excessive hemoglobin suggests hematoma.
Twin-color light (790/915 nm) interrogates Hb and HbO2 via All-Optical Photoacoustic (PA) imaging
Speckle-tolerant Laser sensing (1064 nm) of PA pressure waves
Autonomous Laser Scanning forms hematoma map with onboard GPU
Handheld by Combat Medic for Role 1 care
Graphic User Interface
Role 2 and Role 3 Applications
filtering
Laser ON
Laser OFF