## Slide 1
Introduction
Handheld non-contact laser ultrasound design and implementation
Method
Results
Conclusion
ChenChia Wang1, Feng Jin1, Sudhir Trivedi1, Mark Goncharovsky1, Deepak Patel1, Hayden Diener1, Gary P. Zientara2, Jacob B. Khurgin3, Xue Bai4, Benjamin Punshon-Smith4, and Fow-Sen Choa4
1Brimrose Corp., Baltimore, MD 21152 2US Army Research Institute of Environmental Medicine, Natick, MA 01760
3Dept. of Electrical and Computer Engineering, The Johns Hopkins University, Baltimore, MD 21218 4University of Maryland, Baltimore County, Baltimore, MD 21250
DHA SBIR Sequential Phase II Program #HT942525CE016
Autonomous image scanning, no manual intervention
Photoacoustic (PA) pressure wave generation and Laser signal detection, all-optical, non contact PAI
Visible/ToF cameras for image registration and body contour calibration
Autonomous laser beam scanning over ROI via Photonic IC: NO moving parts
Optical Speckle-tolerant Laser retrieval of PA signatures
Deep learning for US image de-noising
Onboard GPU US image processing, reconstruction
Photonic IC for device compactness
This project is supported by DHA SBIR Sequential Phase II Program under the guidance of Dr. Gary P. Zientara of US Army Research Institute of Environmental Medicine
Development of US image reconstruction algorithms
Development, bui;ld, and validation of tailored electronics
3D Rendering of Prototype
PIC layout design and simulations
Electronic controlled light beam routing and pointing
Operational Applicability : Handheld for Role 1, 2 care,
Wireless communications for waveform sharing and off-line studies
Autonomous operations minimizes human intervention
Alleviates operator skill level requirements
NonContact Ultrasound (US) Imaging provides operational efficiency, ease of transport, acoustic gel free, and operator skill level independent
Autonomous scanning aids triage efficiency
Applies for injured Warfighters with open wounds and/or CBRN contaminations
Device miniaturization by Photonic IC deployment. NO moving parts
Handheld by Combat Medic for Role 1 care
Role 2 and Role 3 Applications
De-noise algorithm improves US image quality