## Slide 1
Validation of Acoustic Phenomenology Modeling Within the Vestibular System
Trevor Mitcham, PhD1, Ethan Parsons, PhD1, Jonathan Richardson PhD1, Michael Collins, MS1, Ion Candel, PhD2, Robert Haupt, MS-MS1
1. MIT Lincoln Laboratory. 2. Massachusetts General Hospital
Learning Objectives
Evaluate the accuracy of a computational model in predicting health effects from directed acoustic energy.
Demonstrate experimental methods used to validate the numerical model.
Discuss potential applications of this approach in developing exposure guidelines and regulations for acoustic directed energy.
Motivation
Safe exposure limits of acoustic DE on vestibular system remain undefined above 20 kHz (human hearing threshold).
  Vestibular organs rely on fluid, ion transport for balance [1].
  Acoustic DE may cause abnormal fluid motion, risking disorienting effects.
Goal: Develop a multiphysics numerical model to predict and explain bioeffects of acoustic DE on the vestibular system.
In this work, phantom studies are used to validate a novel numerical model.
Numerical Model
Multiphysics numerical model captures the complex interactions in the vestibular system.
Simulates vestibular system properties:
  Fluid pressure, electrical potential, and ion movement in response to acoustic DE.
  Finite difference computational model.
  Models rigid, viscous, and fluid media.
Biot Slow Waves
Porous structures found throughout the vestibular organ support Biot Slow wave propagation, impacting acoustic energy transfer [2].
Experimental Validation:
  Sintered glass phantoms (4-36% porosity).
  Transmission ultrasound (US) measured Biot Slow wave propagation.
  Wave velocities and amplitude ratios vary with porosity [2,3].
Results calibrate poroelastic parameters in numerical model.
Diffuse Correlation Spectroscopy (DCS)
DCS is an optical technique using near-infrared (NIR) light to measure flow at depth [4].
  Two fibers correlate scattered light to flow.
  Detects flow as low as 0.08 mm/s in narrow tubes similar to those in the vestibular system
DCS validates numerical model flow predictions in phantom models at depth.
Acoustic Array
Conformal US transducer array measures acoustic signals through the skull.
Array specifications:
  64 hydrophones (1.5 mm aperture).
  Bandwidth 70 kHz-1.9 MHz.
  RF shielded elements and cables.
  Array tested through ex vivo human skull:
    500 Pa source: >30 dB SNR (150-800 kHz).
    350 Pa source: 60 dB SNR (250 kHz).
    0.4 Pa source: 6.8 dB SNR (250 kHz).
    Enables validation of acoustic model predictions through intact skull.
Conclusions
In vitro validation is critical to ensure numerical model accuracy
Advanced sensing techniques (DCS, transcranial US arrays) provide novel tools to benchmark and validate model development.
This simulation validation framework will inform evidence-based guidance for informing safety decisions regarding acoustic DE
References
Angelaki DE, Cullen KE. Vestibular system: the many facets of a multimodal sense. Annu. Rev. Neurosci. 2008 Jul 21;31(1):125-50.
Plona TJ. Observation of a second bulk compressional wave in a porous medium at ultrasonic frequencies. Applied physics letters. 1980 Feb 15;36(4):259-61.
Johnson DL, Plona TJ. Acoustic slow waves and the consolidation transition. The Journal of the Acoustical Society of America. 1982 Aug 1;72(2):556-65.
Durduran T, Yodh AG. Diffuse correlation spectroscopy for non-invasive, micro-vascular cerebral blood flow measurement. Neuroimage. 2014 Jan 15;85:51-63.
Figure 1: Anatomical model of the vestibular system, highlighting the receptors within the semi-circular canals, crista, saccule, and utricle.
Figure 2: 3D mesh of the vestibular organs and cochlea for numerical modelling and phantom design. Left: exterior of the vestibular system. Right: cutaway of the vestibular system showing the semi-circular canals and the vestibule.
Sample | Fast Compressional Sound Speed (m/s) | Slow Compressional Sound Speed (m/s) | Amplitude Ratio (slow/fast)
Water | N/A | N/A | N/A
4% porosity | 4100 m/s | N/A | N/A
16% porosity | 3460 m/s | 890 m/s | 0.322
36% porosity | 2950 m/s | 980 m/s | 0.435
Table 1: Fast and Slow (Biot) compressional wave characteristics in porous glass discs.
Figure 4: A) Graphical depiction of DCS sensing. Light is introduced by a source fiber and received after multiple scattering events in the flowing fluid. B) Experimental setup with milk-filled tubing for optical scattering. C) DCS measurements at different flow rates from (B).
Figure 3: A) Phantom testing with sintered glass disc between US transducers. B) US signal showing the fast compressional wave (orange) and Biot Slow wave (purple) through the 36% porous sample.
Figure 5: A) SNR across full bandwidth from a 500 Pa source through the skull. B) Detected signals from a 350 Pa source (top) and a 0.4 Pa source (bottom) through the skull. C) 64-element conformal array prototype on ex vivo human skull.
DISTRIBUTION STATEMENT C. Distribution authorized to U.S. Government agencies and their contractors; Administrative or Operational Use; 2018. Other requests for this document shall be referred to Defense Health Agency (Combat Casualty Care), 504 Scott St., Fort Detrick, MD 21702-5011.
WARNING: This document may contain technical data whose export is restricted by the Arms Export Control Act (AECA) or the Export Control Reform Act of 2018 (ECRA). Transfer of this data by any means to a non-US person who is not eligible to obtain export-controlled data is prohibited. By accepting this data, the consignee agrees to honor the requirements of the AECA and ECRA. DESTRUCTION NOTICE: For unclassified, limited distribution documents, destroy by any method that will prevent disclosure of the contents or reconstruction of the document.
This material is based upon work supported by the Under Secretary of War for Research and Engineering under Air Force Contract No. FA8702-15-D-0001 or FA8702-25-D-B002. Any opinions, findings, conclusions or recommendations expressed in this material are those of the author(s) and do not necessarily reflect the views of the Under Secretary of War for Research and Engineering.
© 2026 Massachusetts Institute of Technology.
Delivered to the U.S. Government with Unlimited Rights, as defined in DFARS Part 252.227-7013 or 7014 (Feb 2014). Notwithstanding any copyright notice, U.S. Government rights in this work are defined by DFARS 252.227-7013 or DFARS 252.227-7014 as detailed above. Use of this work other than as specifically authorized by the U.S. Government may violate any copyrights that exist in this work.